## Slide 1: Image Formation III Chapter 1 (Forsyth&Ponce) Cameras “Lenses”
Guido Gerig
CS 6320 S2015
(Acknowledgements:
modified from Marc Pollefeys, UNC Chapel Hill
Some materials from Prof. Trevor Darrell, trevor@eecs.berkeley.edu

## Slide 2: Pinhole size / aperture
Smaller
Larger
How does the size of the aperture affect the image we’d get?
K. Grauman

## Slide 3: Pinhole vs. lens
K. Grauman
Shrinking hole -> sharper, but less light

## Slide 4: Adding a lens
A lens focuses light onto the film
  Rays passing through the center are not deviated
  All parallel rays converge to one point on a plane located at the focal length f
Slide by Steve Seitz
focal point
f

## Slide 5: Field of view
Angular measure of portion of 3d space seen by the camera
Images from http://en.wikipedia.org/wiki/Angle_of_view
K. Grauman

## Slide 6: Field of view depends on focal length
As f gets smaller, image becomes more wide angle
  more world points project onto the finite image plane
As f gets larger, image becomes more telescopic
  smaller part of the world projects onto the finite image plane
from R. Duraiswami

## Slide 7: Cameras with lenses
focal point
F
optical center
(Center Of Projection)
A lens focuses parallel rays onto a single focal point
Gather more light, while keeping focus; make pinhole perspective projection practical
K. Grauman

## Slide 8
Lenses
Snell’s law,
Law of refraction
n1 sin a1 = n2 sin a2
n1, n2 : refraction indices
Descartes’ law

## Slide 9
Paraxial (or first-order) optics
Snell’s law:
n1 sin a1 = n2 sin a2
Small angles:
n1 a1  n2a2

## Slide 10
Thin Lenses
spherical lens surfaces; thickness << radii; same refractive index on both sides; all rays emerging from P and passing through the lens are focused at P’. Let n1=1 (vaccuum) and n2=n.

## Slide 11
Thin Lenses
http://www.phy.ntnu.edu.tw/java/Lens/lens_e.html
spherical lens surfaces; thickness << radii; same refractive index on both sides; all rays emerging from P and passing through the lens are focused at P’. Let n1=1 (vacuum) and n2=n.

## Slide 12
Thick Lens

## Slide 13: Focus and depth of field
Image credit: cambridgeincolour.com

## Slide 14: Focus and depth of field
Depth of field: distance between image planes where blur is tolerable
Thin lens: scene points at distinct depths come in focus at different image planes.
(Real camera lens systems have greater depth of field.)
Shapiro and Stockman
“circles of confusion”

## Slide 15: Focus and depth of field
How does the aperture affect the depth of field?
A smaller aperture increases the range in which the object is approximately in focus
Flower images from Wikipedia http://en.wikipedia.org/wiki/Depth_of_field
Slide from S. Seitz

## Slide 16
The depth-of-field


## Slide 17
The depth-of-field


## Slide 18
The depth-of-field

yields
Similar formula for

## Slide 19
The depth-of-field
decreases with d+, increases with Z0+

strike a balance between incoming light and
sharp depth range

## Slide 20
Deviations from the lens model
3 assumptions :
1. all rays from a point are focused onto 1 image point
2. all image points in a single plane
3. magnification is constant
deviations from this ideal are aberrations


## Slide 21
Aberrations
chromatic : refractive index function of
wavelength
2 types :
1. geometrical
2. chromatic
geometrical : small for paraxial rays

study through 3rd order optics

## Slide 22
Geometrical aberrations
spherical aberration
astigmatism
distortion
coma
aberrations are reduced by combining lenses


## Slide 23
Spherical aberration
rays parallel to the axis do not converge
outer portions of the lens yield smaller
focal lenghts


## Slide 24: Astigmatism
Different focal length for inclined rays

## Slide 25: Distortion
magnification/focal length different
for different angles of inclination
Can be corrected! (if parameters are know)
pincushion
(tele-photo)
barrel
(wide-angle)

## Slide 26: Coma
point off the axis depicted as comet shaped blob

## Slide 27
Chromatic aberration
rays of different wavelengths focused
in different planes
cannot be removed completely
sometimes achromatization is achieved for
more than 2 wavelengths


## Slide 28
Lens materials
reference wavelengths :
F = 486.13nm
d = 587.56nm
C = 656.28nm
lens characteristics :
1. refractive index nd
2. Abbe number Vd= (nd - 1) / (nF - nC)
typically, both should be high
allows small components with sufficient refraction
notation : e.g. glass BK7(517642)
nd = 1.517 and Vd= 64.2


## Slide 29
Lens materials
additional considerations :
humidity and temperature resistance, weight, price,...

Crown Glass
Fused Quartz & Fused Silica
Plastic (PMMA)
Calcium Fluoride
Saphire
Zinc Selenide
6000
18000
Germanium 14000
9000
100 200 400 600 800 1000 1200 1400 1600 1800 2000 2200 2400
WAVELENGTH (nm)

## Slide 30
Vignetting