## Slide 1: Volume Rendering
Chris Johnson
Guoning Chen Chuck Hansen
Bob Laramee Josh Levine Han-Wei Shen Alex Teleau

## Slide 2: Reading Assignment: Visualization Handbook Overview of Volume Rendering Arie Kaufman and Klaus Mueller page 127 Multidimensional Transfer Functions for Volume Rendering Joe Kniss, Gordon Kindlmann, and Charles D. Hansen page 189

## Slide 3: Limitations of Isosurfaces

## Slide 4
Isosurfacing is "binary"
  What about points inside isosurface?
  How does each voxel contribute to the image?
Is a hard, distinct boundary necessarily appropriate for the visualization task?
Isosurface
Volume Rendering
Slice

## Slide 5
Isosurfacing is poor for ...
  Measured, "real-world" (noisy) data
  Amorphous, "soft" objects
http://vis.cs.ucdavis.edu/gallery/Yu/combustion/
http://www.cg.informatik.uni-siegen.de/

## Slide 6: Why Volume Rendering?
Allows every voxel to contribute to image
Provides greater flexibility
Marc Levoy, Display of Surfaces from Volume Data, 1988

## Slide 9: Volume Rendering

## Slide 11: Pipelines: Isosurfacing vs. Volume Rendering
the standard pipeline:
no intermediate geometric structures
Volume Data
Triangles
Rendered Image
isosurface
extraction
surface
rendering
volume
rendering
standard graphics operations:
shading, lighting, compositing
Rendered Image
Volume Data

## Slide 12
What is Volume Rendering?
  Any rendering process which maps from volume data to an image (without introducing binary distinctions or intermediate geometry)
Core question (for the visualizer):
  How do you make the data visible?
  Answer: color and opacity

## Slide 13: Direct 3D Representation of Volume Data
Data considered to represent a semi-transparent light-emitting medium
  Also gaseous phenomena can be simulated
Approaches based on laws of physics (emission, absorption, scattering)
Volume data used as a whole (look inside, see all interior structures)

## Slide 14
DVR: Render volume without extracting any surfaces
Map scalar values to optical properties (color, opacity)
Needs an optical model
Solve volume rendering integral for viewing rays into the volume

## Slide 15: Volume Ray Casting

## Slide 16: Direct Volume Visualization
Ray Casting: the value of each pixel in the image is determined by sending a ray through the pixel into the scene (image order volume rendering)

## Slide 18: Image order approach
Image Plane
For each pixel {
calculate color of the pixel
}
Data Set
Eye

## Slide 21: Compositing

## Slide 22
cb = (1,0,0)
ab = 0.9
cf = (0,1,0)
af = 0.4
?
c = af*cf + (1 - af)*ab*cb
a = af + (1 - af)*ab
Over operator
Alvy Ray Smith (1970s)
Permutation
ci = aiCi

## Slide 23
cb = (1,0,0)
ab = 0.9
cf = (0,1,0)
af = 0.4
cred = 0.4*0 + (1-0.4)*0.9*1 = 0.6*0.9 = 0.54
cgreen = 0.4*1 + (1-0.4)*0.9*0 = 0.4
cblue = 0.4*0 + (1-0.4)*0.9*0 = 0
a = 0.4 + (1 – 0.4)*(0.9) = 0.4 + 0.6*0.9
c = (0.54,0.4,0)
a = 0.94
c = af*cf + (1 - af)*ab*cb
a = af + (1 - af)*ab
over operator

## Slide 24
c2 = (1,0,0)
a2 = 0.9
c1 = (0,1,0)
a1 = 0.4
cb = (0.54,0.4,0)
ab = 0.94
?
cf = (0,1,1)
af = 0.4
c = af*cf + (1 - af)*ab*cb
a = af + (1 - af)*ab
over operator

## Slide 25
c2 = (1,0,0)
a2 = 0.9
c1 = (0,1,0)
a1 = 0.4
cb = (0.54,0.4,0)
ab = 0.94
cf = (0,1,1)
af = 0.4
cred = 0.4*0 + (1-0.4)*0.94*0.54 = 0.6*0.94*.54 = 0.30
cgreen = 0.4*1 + (1-0.4)*0.94*0.4 = 0.6*0.94*.4 = 0.23
cblue = 0.4*1 + (1-0.4)*0.94*0 = .4
a = 0.4 + (1 – 0.4)*(0.94) = 0.4 + 0.6*0.94) = .964
c = af*cf + (1 - af)*ab*cb
a = af + (1 - af)*ab
over operator

## Slide 26
c2 = (1,0,0)
a2 = 0.9
c1 = (0,1,0)
a1 = 0.4
cb = (0.54,0.4,0)
ab = 0.94
cf = (0,1,1)
af = 0.4
c = (0.3,0.23,0.4)
a = 0.964
c = af*cf + (1 - af)*ab*cb
a = af + (1 - af)*ab
over operator

## Slide 27: Order Matters!
c = (0.3,0.23,0.4)
a = 0.964
c = (0.3,0.23,0.23)
a = 0.964

## Slide 28
Grassman's 2nd Law of Color Science:
The appearance of a mixture of light made from two components changes if either component changes. Corollary: A mixture of two colored lights that are non-complementary result in a mixture that varies in hue with relative intensities of each light and in saturation according to the distance between the hues of each light.
This is where the order comes in. Say we have Red and Green lights producing Yellow. The Yellow will be influenced by the saturation and intensity of Red and Green.

## Slide 29: Pixel Compositing Schemes
depth
max intensity
accumulate
average
first
intensity

## Slide 30: Pixel Compositing Schemes
depth
max intensity
accumulate
average
first
intensity
Exact Isosurface

## Slide 31: Pixel Compositing Schemes
depth
max intensity
accumulate
average
first
intensity
Synthetic Reprojection
Similar to X-rays

## Slide 32: Pixel Compositing Schemes
depth
max intensity
accumulate
average
first
intensity
maximum intensity projection (MIP)
Used in PET and Magnetic Resonance Angiograms

## Slide 33: Pixel Compositing Schemes
depth
max intensity
accumulate
average
first
intensity
color to distinguish structures
opacity to show inside

## Slide 34: Modeling Light

## Slide 35: Direct Volume Rendering
Simulate light transport through a continuous volume
Data are interpolated from the samples at the grid points
Optical properties such as colors and opacities are assigned to the interpolated data
Optical properties must be integrated along each viewing ray
c2
c3
c1
X

## Slide 36: Optical Model
Absorption Model
Emission Model
Absorption + Emission
Participating medium (the voxels) can absorb, emit, or both absorb and emit light
How much light will reach the eye?
S = 0
S = D

## Slide 37: Absorption Only
The simplest participating medium
Consists of perfectly black particles that absorb all the light that they intercept
Assume
  each particle has an area of A = pr2
  Number of particles per unit volume = r
  A small cylindrical slab with a base area E and thickness Ds
E
Ds
A = pr2
  Total number of particles = E Ds r
  Total area occluded by particles = A E Ds r
  The fraction of occluded area = AEDsr / E = A Ds r
Solve this ODE
d I(s)
ds
= - I(s) x A Ds r(s) = - A r (s) I(s)
Ds

## Slide 38: Absorption Only
The simplest participating medium
Consists of perfectly black particles that absorb all the light that they intercept
Assume
  each particle has an area of A = pr2
  Number of particles per unit volume = r
  A small cylindrical slab with a base area E and thickness Ds
E
Ds
A = pr2
dI
ds
= - A r (s) I(s)
Solve this ODE

## Slide 39: Absorption Only
E
Ds
A = pr2
: extinction coefficient
I0 = Initial light intensity
I0
Can be seen as the transparency, or
1 – opacity of the medium from 0 to s

## Slide 40: Emission Only
Each particle will glow diffusively with an intensity C
In a small cylindrical slab, the
total area occupied by the
particles is AEDsr
So the glow flux will be CAEDsr
Then the glow per unit area is CAEDsr /E = CADsr
E
Ds
A = pr2
dI
ds
= C(s) A r(s) = C(s)t(s) = g(s)
Solve this ODE

## Slide 41: Emission Only
Each particle will glow diffusively with an intensity C
In a small cylindrical slab, the
total area occupied by the
particles is AEDsr
So the glow flux will be CAEDsr
So the glow per unit area is CAEDsr /E = CADsr
dI
ds
= C(s) A r(s) = C(s)t(s) = g(s)
Solve this ODE
E
Ds
A = pr2

## Slide 42: Emission plus Absorption
Simply add emission and absorption together
dI
ds
= C(s)t(s) - A r (s) I(s) = g(s) – t(s)I(s)
E
Ds
A = pr2
Solve this ODE
emission
absorption
S = 0
S = D

## Slide 43: Put It All Together
Absorption only:
Emission only:
Emission plus absorption:
S = 0
S = D

## Slide 44: Look More Closely
: background light
: extinction coefficient at t , related to the rate that light
is occluded
: total distance light will travel
: transparency of medium between 0 and D
: opacity of medium between 0 and D
: source term at point s, typically derived from the data value
S = 0
S = D

## Slide 45: Discrete Implementation
Numerical integration:
Dx = Xi – Xi-1
X0 X1 X2 X3 X4 X5 …
(Riemann Sum)
(Remember )

## Slide 46: Discrete Implementation
S = 0
S = D
g1 g2 g3 g4 g5 g6 g7 g8 g9 g10 …
a1 a2 a3 a4 a5 a6 a7 a8 a9 a10 …
= gn + (1-an)(gn-1+(1-an-1)(gn-2+ (1-an-2(…. a2(g2+(1-a1)(g1+I0)))))…)))))
This is called - Back to Front Compositing

## Slide 47: Discrete Implementation
S = 0
S = D
g1 g2 g3 g4 g5 g6 g7 g8 g9 g10 …
a1 a2 a3 a4 a5 a6 a7 a8 a9 a10 …
= gn + (1-an)(gn-1+(1-an-1)(gn-2+ (1-an-2(…. (1-a2)(g2+(1-a1)(g1+I0)))))…)))))
( )

## Slide 48: Ray Casting Algorithm
For each pixel
  Cast a ray into the volume
  Linearly interpolate data values from cell (voxel) corners
  Convert the data values to optical properties (color and opacity)
  Composite the optical properties
  Return the final color
X
g1
g2
g3

## Slide 49: Shading and Classificaton
Shading: computer a color for every sample in the volume
Classification: computer an opacity for every sample in the volume
This is often done through a table (transfer function) lookup
f(xi)
c(xi), a(xi)

## Slide 50: Shading
Use the Phong illumination model
illumination = ambient + diffuse + specular
q q
Sample i
f
V
R
N
L
= C(xi) x Ia + C(xi) x Id x (N.L) + C(xi) x Is x (R.V)n
C(xi) : color of sample i
Ia, Id, Is: light’s ambient, diffuse, and specular colors (usually set as white)
N: normal at sample i
V: vector from sample point to eye
L: light vector, from sample to light source
R: reflection vector of light vector
n: shininess

## Slide 51: Normal Estimation
How to compute the sample normal N?
  Normal: a vector that is perpendicular to the local surface, which is the gradient of the sample point
Compute the gradient G at the cell corners using central difference
Linearly interpolate the gradients

## Slide 52: Classification
Classification: mapping from data values to opacities
  Region of interest: high opacity
  Rest: translucent or transparent
The opacity function, or called transfer function, is given by the user

## Slide 53: Ray Sampling
c1
c2
c3
Sample the volume at discrete
points along the ray
Perform tri-linear interpolation to get
the sample values
Look up the transfer function to
get the color and opacity
Compositing the color/opacity
(front-to-back or back-to-front)

## Slide 54: Back-to-Front Compositing
c1
c2
c3
The initial pixel color = Black
Back-to-Front compositing:
use ‘under’ operator
C = C1 ‘under’ background
C = C2 ‘under C
C = C3 ‘under C
…
Cout = Cin * (1-a(x)) + C(x)*a(x)
(this is the alpha blending formula)

## Slide 55
c1
c2
c3
Front-to-Back compositing:
use ‘over’ operator
C = background ‘over’ C1
C = C ‘over’ C2
C = C ‘over’ C3
…
Cout = Cin + C(x) a(x) *(1- ain);
aout = ain + a(x) *(1-ain)
Front-to-Back Compositing

## Slide 56
We perform a numerical approximation of volume rendering integral
Idea: resample volume at equispaced intervals along the ray
  Use trilinear interpolation

## Slide 57: Ray-Casting Highlights
Advantages
  Simple algorithm
  Inherently parallel
  Can add features (like a ray-tracer)
Disadvantages
  Slow (lots of rays, lots of samples)
  Must sample densely
  Requires data set in memory

## Slide 58: Object-Ordered Approaches

## Slide 59: Object order approach
Image Plane
For each slice {
calculate contribution to the image
}
Data Set
Eye

## Slide 60: Object Order: Splatting
Main Idea: Throw voxels to the image
  Front-To-Back or Back-To-Front
Original method - fast, poor quality, many many improvements since then!
  Crawfis’93: textured splats
  Swan’96, Mueller’97: anti-aliasing
  Mueller’98: image-aligned sheet-based splatting
  Mueller’99: post-classified splatting
  Huang’00: new splat primitive: FastSplats

## Slide 61: Splatting
Volume = field of 3D interpolation kernel
  One kernel at each grid voxel
Each kernel leaves a 2D footprint on screen
  Voxel contribution = footprint ·(C, opacity)
Weighted footprints accumulate into image
voxel kernels
screen footprints = splats
screen

## Slide 62: Splatting
Volume = field of 3D interpolation kernel
  One kernel at each grid voxel
Each kernel leaves a 2D footprint on screen
  Voxel contribution = footprint ·(C, opacity)
Weighted footprints accumulate into image
voxel kernels
screen footprints = splats
screen

## Slide 63: Splatting
Volume = field of 3D interpolation kernel
  One kernel at each grid voxel
Each kernel leaves a 2D footprint on screen
  Voxel contribution = footprint ·(C, opacity)
Weighted footprints accumulate into image
voxel kernels
screen footprints = splats
screen

## Slide 64: Splatting
Volume = field of 3D interpolation kernel
  One kernel at each grid voxel
Each kernel leaves a 2D footprint on screen
  Voxel contribution = footprint ·(C, opacity)
Weighted footprints accumulate into image
voxel kernels
screen footprints = splats
screen

## Slide 65: Ray-casting - revisited
color c = c s s(1 - ) + c
opacity  =  s (1 - ) + 
1.0
object (color, opacity)
volumetric compositing
Interpolation kernel

## Slide 66: Ray-casting - revisited
(Ideally) we would reconstruct the continuous volume (cloud) using the interpolation kernel h:
Then we would compute the analytic integral along a ray r:
This can only be approximated by discretization

## Slide 67: Splatting - Principal Idea
This last equation
can be rewritten in the following way:
Splatting Kernel or “Splat”
Which can be computed analytically: known as footprint

## Slide 68: Footprint Extent
Approximate the 3D kernel (h(x,y,z))extent by
a sphere

## Slide 69: Footprint Table
A popular kernel is a three-dimensional Gaussian
(radially symmetric)
As 1D integration of 3D Gaussian is still a 2D Gaussian –
we can just skip the Z integration and evaluate the Gaussian
function on 2D image space after voxel projection
Generic footprint
table
preprocessing

## Slide 70: View-dependent footprint
It is possible to transform a sphere kernel into
A ellipsoid
The projection of an
ellipsoid is an ellipse
We need to transform the
generic footprint table
to the ellipse

## Slide 71: View-dependent footprint (2)

## Slide 72: Example Footprint at Different Resolutions

## Slide 73: Footprint - principal idea
Draw each voxel as a cloud of points (footprint) that spreads the voxel contribution across multiple pixels.
Larger footprint -> larger spatial kernel extent -> lower frequency components -> more blurring
  Large pixel/voxel ratio

## Slide 74: Splatting - Evaluation
Advantages:
  Footprints can be pre-integrated
  Fast: voxel interpolation is in 2D on screen
  More accurate integration (analytic for X-ray)
  More accurate reconstruction (better kernels)
  Only relevant voxels must be projected
Disadvantages:
  Blurry images for zoomed views!
  High fill-rate for zoomed splats!
  Result is wrong where filter overlap

## Slide 75: Texture-Mapping

## Slide 76: Texture Mapping
Idea: Use image data to make up for lack of complexity in the modeling process
Pixels get additional coordinate information (texture coordinates) which index an image.
Graphics pipelines are specifically designed to take of advantage of this concept, with fast access to memory and builtin interpolation, texture mapping units
3D textures are a common way to accelerate volume rendering
http://www.wolfram.com/mathematica/new-in-8/enhanced-2d-and-3d-graphics/

## Slide 77: Review on Texturing (Bilinear Interpolation)

## Slide 83: Texture-based
Volume rendering by 2D texture mapping
  Use planes parallel to “base plane” (front face of volume which is most orthogonal to view ray)
  Draw textured rectangles using bilinear interpolation
  Render back-to-front using compositing

## Slide 87: 3D Textures
Voxel data becomes a 3D Texture Object
  Trilinear Interpolation in Hardware
  Uses an arbitrary number of slices parallel to the image plane
  Back-to-front compositing used just as in 2d texturing
  Can be limited by the size of the texture memory

## Slide 91: Shear-Warp

## Slide 94: Orthographic vs. Perspective Projections
Dianne Hansford

## Slide 97: Shear-Warp Evaluation
Advantages
  Pixel scanlines (intermediate) are parallel to voxel rows
  All voxels in a slice are scaled uniformly
  Therefore, the sampling rate is uniform within each volume slice
  Similar to template-based volume ray casting (Yagel 91)
Disadvantages
  Affine projection (no perspective)
  Compute time (relative to splatting & slice-based)

## Slide 98: Computational Strategies
Image Order:
  Ray casting (many options)
Object Order:
  Splatting, Texture mapping
Combinations:
  Shear-warp