## Slide 1: Towards data-optimal storage, retrieval, and algorithms
Duong (/zwong/) Hoang (Univ of Utah)
Peter Lindstrom (Lawrence Livermore National Laboratory)
Peer-Timo Bremer (Lawrence Livermore National Laboratory)
Valerio Pascucci (Univ of Utah)

## Slide 2: Problem
Rapid increase in computing power, thus data size
Need serious computing resources to visualize/analyse data
  Run ParaView/VisIt on computer clusters
Alternatively, work on a reduced representation of data
  Low resolution
  Low precision
  Suffice for surprisingly many tasks

## Slide 3: IDX + zfp
Combine two data-reduction techniques: IDX (for spatial resolution) and zfp (for numerical precision)
IDX sub-samples the structured data
zfp reduces bit-precision of the data
Subsampling is also one form of compression
Original
Sub-sampling
Reduced color bits

## Slide 4: IDX
  Re-arranges samples to store those belonging to the same “resolution” together on disk
    Use Z-like space filling curves to preserve spatial locality
    This order is called Hierarchical Z (or HZ)
  No redundant data (e.g., pyramids)
  Supports fast reads of low-resolution data (avoids disk seeks)
  Supports progressive data streaming
  Implemented in ViSUS software
    Used successfully in many real-world analysis

## Slide 5: zfp
Break the input volume into 4x4x4 blocks
Orthogonal block transform on each block
  De-correlates the numbers in the block
  zfp: special constants facilitates fast implementation
Many high-frequency co-efficients are near 0
  Efficient (embedded) coding of these co-efficients
  Lossy by throwing away trailing bits in the encoding
Embedded coding allows decompression of “partial” bit streams
  Read just enough data to decompress, say, at 1 bit/double
(this is the DCT transform, used in JPEG)

## Slide 6: Embedded Coding
bit 1 bit 2 bit 3 bit 4
1/16 2/16 4/16 8/16
IDX
zfp
Any prefix segment of the data contains useful information
Keep reading incrementally to obtain “better” data

## Slide 7: Challenges
zfp requires data in each block to be smooth, while IDX samples scatter sparsely at low resolutions

## Slide 8: Two approaches
Block compression (a)
  Poor(er) quality due to sparse data
  No read penalty
Brick compression (b)
  Best quality
  Have to read whole “bricks” to get (a few) samples within

## Slide 9: Interleaving bit planes
B1-bit1 | B2-bit1 | B3-bit1 | B4-bit1 | B1-bit2 | B2-bit2 | B3-bit2 | B4-bit2
B1 | B2 | B3 | B4
2 bits per value * 64 = 128 bits
64 bits
Just need to fetch (the first) half of the compressed data if the required precision is only 1 bit/value

## Slide 10: Datasets
Miranda
Density field
384 x 384 x 256 x 64-bit
Combustion
Heat release rate field
512 x 512 x 256 x 64-bit
Combustion
OH field
512 x 512 x 256 x 64-bit
Synthetic
Sine function
512 x 512 x 512 x 32-bit

## Slide 11: Interpret brick samples
Low-resolution bricks exhibit “uneven” sampling patterns
We can choose to throw away “unneeded” samples
Need to investigate different interpolation schemes

## Slide 12: I/O penalty for brick compression (1)
How to benchmark disk I/O
  Clear disk buffer (managed by disk controller, on hardware)
    Read (and write) a reasonably large (> 16 MB) file
  Clear disk cache (managed by OS, in RAM)
    Mac, Linux: purge command
    Windows: use a Win32 API to empty standby list
High resolution timers (clock() function has a resolution of ~ 15ms)
  Linux: clock_gettime(CLOCK_MONOTONIC)
  Mac: mac_absolute_time()
  Windows: QueryPerformanceCounter()
  C++ 11’s chrono::high_resolution_clock
Measure multiple times (~20) and take the median

## Slide 13: I/O penalty for brick compression (2)
Chart: Total time (I/O + Computation + Decompression) Smaller is better
| 64x32x32 | 128x32x32 | 128x64x32 | 128x64x64 | 256x64x64 | 256x128x64 | 256x128x128 | 512x128x128 | 512x256x128 | 512x256x256
Normal IDX | 104 | 125 | 124 | 87 | 143 | 234 | 457 | 890 | 1843 | 3630
Bit rate 16 | 413 | 612 | 1128 | 1978 | 1978 | 1978 | 1978 | 1978 | 1978 | 1978
Bit rate 8 | 278 | 406 | 686 | 1220 | 1220 | 1220 | 1220 | 1220 | 1220 | 1220
Bit rate 4 | 186 | 271 | 462 | 754 | 754 | 754 | 754 | 754 | 754 | 754
Bit rate 2 | 174 | 183 | 327 | 583 | 583 | 583 | 583 | 583 | 583 | 583
Bit rate 1 | 191 | 173 | 258 | 501 | 501 | 501 | 501 | 501 | 501 | 501
512x512x256 volume, double precision
Compressed to 16 bits/double
Brick compression is better for high-resolution data at low bit rates

## Slide 14: Decompression time
Chart: Breakdown of processing time at different resolutions
| Bit rate 16 | Bit rate 8 | Bit rate 16 | Bit rate 8 | Bit rate 16 | Bit rate 8 | Bit rate 16 | Bit rate 8 | Bit rate 16 | Bit rate 8 | Bit rate 16 | Bit rate 8 | Bit rate 16 | Bit rate 8 | 32x16x16 |  | 64x16x16 |  | 64x32x16 |  | 64x32x32 |  | 128x32x32 |  | 128x64x32 |  | 128x64x64
I/O | 126 | 67 | 125 | 66 | 126 | 116 | 223 | 136 | 259 | 171 | 487 | 260 | 726 | 390
Computation | 44 | 25 | 36 | 33 | 57 | 24 | 65 | 51 | 113 | 64 | 163 | 94 | 299 | 160
Decompression | 21 | 15 | 35 | 29 | 65 | 53 | 125 | 91 | 240 | 171 | 478 | 332 | 953 | 670
512x512x256 volume, double precision
Compressed to 16 bits/double
Decompression time is significant (although should be quite faster with new code)
Notice that I/O time does not scale expectedly

## Slide 15: I/O speed when reading bricked data
Chart: I/O Speed Larger is better
| Resolution 7 | Resolution 6 | Resolution 5 | Resolution 4 | Resolution 3 | Resolution 2 | Resolution 1
Normal IDX | 71 | 83 | 88 | 87 | 81 | 78 | 79
Bit rate 16 | 8 | 16 | 31 | 35 | 61 | 65 | 88
Bit rate 8 | 7 | 15 | 17 | 29 | 46 | 61 | 82
Bit rate 4 | 7 | 14 | 26 | 26 | 43 | 53 | 87
Bit rate 2 | 6 | 8 | 21 | 19 | 53 | 62 | 79
Bit rate 1 | 0.7 | 0.9 | 4 | 5 | 42 | 59 | 69

## Slide 16: IDX blocks
4 blocks, each having 4 samples
Header 1 | Header 2 | Header 3 | Header 4
Blocking
allows flexibility in I/O and storage
acts as a kind of index for fast sub-volume queries
saves space when the a volume’s dimension(s) is not a power of 2
Usually headers take up a tiny space compared to actual data (on the order of KB)

## Slide 17: Block access time
Chart: Time at which a block is accessed as a function of block position
Hypothesis: the “jump” is seek time due to constantly jumping back and forth between IDX block headers and block data
Seek time on a typical hard 7200rpm hard drive is around 15 ms. Numbers seem to check out.
Seek does not occur at every read because headers are small and thus would be partially cached in RAM

## Slide 18: Block compression
Keep data in each block in row-major order (instead of Z order)
Only compress the last 6 HZ levels (where the samples are still somewhat coherent)
  The uncompressed data is only 1/64 the original

## Slide 19: Ratio of RMS error (block/brick)
Chart: RMS error ratio (IDX block compression/brick compression)
Bit rate 1 | 3.3424 | 4.3595 | 5.567 | 7.2858 | 8.0497 | 7.9005 | 7.3206
Bit rate 2 | 5.5259 | 7.4999 | 9.928 | 13.2681 | 16.2495 | 17.4281 | 16.7125
Bit rate 4 | 8.2028 | 11.368 | 15.3921 | 20.9103 | 28.5818 | 34.4065 | 36.6556
Bit rate 8 | 9.7138 | 13.5346 | 18.3606 | 25.0572 | 36.8011 | 46.0727 | 53.3759
Bit rate 16 | 9.4738 | 13.1369 | 17.703 | 24.0638 | 35.2738 | 43.7653 | 51.0189
Not corresponds to plots on the left, but just to demonstrate visually what a large RMS error would look like

## Slide 20: Fixed-bit-budget comparison
Attempt at an apple-to-apple comparison of brick and block compression schemes
Fix a query budget (i.e. cannot read more than x MB)
Each scheme determines the best possible bit rate to query at each resolution
Upsample the queried data to full resolution and compare with original data (using RMS error)
Expect some trade-offs
  Brick scheme would need to use lower bit rates to compensate for reading more samples (64x at max)
  Block scheme would need to increase its bit rate to compensate for larger compression errors

## Slide 21: Fixed-bit-budget comparison (budget = 1 MB)
Chart: Data transfer budget = 1 MB
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
Block | 2.1475 | 0.13537 | 0.033638 | 0.019351 | 0.016005 | 0.018497 | 0.023008 | 0.040784 | 0.058637 | 0.071762
Brick | 2.1557 | 2.1557 | 2.1557 | 2.1557 | 2.1557 | 2.1557 | 2.1557 | 0.11158 | 0.057953 | 0.071659

## Slide 22: Fixed-bit-budget comparison (budget = 3 MB)
Chart: Data transfer budget = 3 MB
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
Block | 0.032909 | 0.017108 | 0.0094182 | 0.0068098 | 0.012588 | 0.018155 | 0.023006 | 0.040784 | 0.058637 | 0.071762
Brick | 0.013074 | 0.012272 | 0.011981 | 0.011977 | 0.016119 | 0.020702 | 0.025133 | 0.040498 | 0.058612 | 0.07176

## Slide 23: Fixed-bit-budget comparison (budget = 9 MB)
Chart: Data transfer budget = 9 MB
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
Block | 0.0074018 | 0.0042168 | 0.0045535 | 0.0059398 | 0.012565 | 0.018155 | 0.023006 | 0.040784 | 0.058637 | 0.071762
Brick | 0.0010864 | 0.0010864 | 0.004652 | 0.006082 | 0.012554 | 0.018064 | 0.022851 | 0.040779 | 0.058636 | 0.071762

## Slide 24: Fixed-bit-budget comparison (budget = 27 MB)
Chart: Data transfer budget = 27 MB
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
Block | 0.00069156 | 0.0028825 | 0.0044856 | 0.0059393 | 0.012565 | 0.018155 | 0.023006 | 0.040784 | 0.058637 | 0.071762
Brick | 3.9817e-05 | 0.0028829 | 0.004488 | 0.0059418 | 0.012565 | 0.018154 | 0.023004 | 0.040784 | 0.058637 | 0.071762

## Slide 25: Future research directions
Current upsampling method is “IDX-aware” tri-linear interpolation
Cubic, Laplacian, bi-Laplacian interpolants?
  Reduce as much as possible the errors caused by upsampling
Perform reasonably complex, qualitative analysis on reduced precision and reduced resolution inputs
  RMS error is not enough
Understand better the trade-offs between bit rate and resolution

## Slide 26: In the long run
Data storage format that supports data-optimal queries
  Do not fetch every bit plane if only need a few bits per sample
  Do not fetch every sample if only need every eighth sample
  Adaptively fetch more bits/samples if necessary
Map a “catalog” of analysis tasks onto the 2D space of numerical precision and spatial resolution
  Example: volume rendering may tolerate less precise data, while derivative computation may work better with somewhat low resolution data
  Let system automatically suggests optimal bit precision/resolution

## Slide 27: The end
Thank you
Questions?