## Slide 1: Linear complexity of finite element method based forward modeling in bioelectromagnetism
Lecture on Nov.26, 2024
Carsten Wolters
Institut für Biomagnetismus und Biosignalanalyse, Westf. Wilhelms-Universität Münster, Germany
Notes: Tensor weiter erlaeutern
Zeitableitung
Programmlaenge, 1Mill.
WM-Rendering->5000 nodes
1:10 raus und anfangs erwaehnen

## Slide 2
Linear complexity for FEM forward modeling: Transfer matrices
Fast FE solver methods
Structure of the lecture

## Slide 3: Link to own work for transfer matrices:
[Wolters, Grasedyck & Hackbusch, Inverse Problems, 2004]
Notes: PEBBLES: Parallel and Element Based grey Box Linear Equation Solver

## Slide 4: EEG transfer matrix
[Wolters, Grasedyck & Hackbusch, Inverse Problems, 2004]
[Weinstein, Zhukov & Johnson, Annals Biomed. Eng.,2000]
Notes: D: electric displacement
rho: electric free charge density
E: electric field
B: magnetic induction
mu: magnetic permeability (vacuum)
j: electric current density
Phi: electric scalar potential
Psi: magnetic flux
A: magnetic vector potential
divA=0: Coulomb’s gauge
conductor loop

## Slide 5: MEG transfer matrix
[Wolters, Grasedyck & Hackbusch, Inverse Problems, 2004]
Notes: D: electric displacement
rho: electric free charge density
E: electric field
B: magnetic induction
mu: magnetic permeability (vacuum)
j: electric current density
Phi: electric scalar potential
Psi: magnetic flux
A: magnetic vector potential
divA=0: Coulomb’s gauge
conductor loop

## Slide 6: MEG transfer matrix
[Wolters, Grasedyck & Hackbusch, Inverse Problems, 2004]
Notes: D: electric displacement
rho: electric free charge density
E: electric field
B: magnetic induction
mu: magnetic permeability (vacuum)
j: electric current density
Phi: electric scalar potential
Psi: magnetic flux
A: magnetic vector potential
divA=0: Coulomb’s gauge
conductor loop

## Slide 7: MEG transfer matrix
[Wolters, Grasedyck & Hackbusch, Inverse Problems, 2004]
Notes: D: electric displacement
rho: electric free charge density
E: electric field
B: magnetic induction
mu: magnetic permeability (vacuum)
j: electric current density
Phi: electric scalar potential
Psi: magnetic flux
A: magnetic vector potential
divA=0: Coulomb’s gauge
conductor loop

## Slide 8: Computing the transfer matrices
[Wolters, Grasedyck & Hackbusch, Inverse Problems, 2004]
Notes: der Tensor muss erklärt werden!!

## Slide 9: Outline
Linear complexity for FEM forward modeling: Transfer matrices
Fast FE solver methods

## Slide 10
[Wolters, Vorlesungsskriptum, Chapter 7.2]
[Wolters, Kuhn, Anwander & Reitzinger, Comp. Vis. Sci.., 2002]
[Lew, Wolters, Dierkes, Roer & MacLeod, Appl.Num.Math., 2009]
Link to this work:
Notes: PEBBLES: Parallel and Element Based grey Box Linear Equation Solver

## Slide 11: FEM solver aspects
[Wolters, Vorlesungsskriptum, Chapter 7.2]
[Wolters, Kuhn, Anwander & Reitzinger, Comp. Vis. Sci.., 2002]
[Lew, Wolters, Dierkes, Roer & MacLeod, Appl.Num.Math., 2009]
Notes: D: electric displacement
rho: electric free charge density
E: electric field
B: magnetic induction
mu: magnetic permeability (vacuum)
j: electric current density
Phi: electric scalar potential
Psi: magnetic flux
A: magnetic vector potential
divA=0: Coulomb’s gauge
conductor loop

## Slide 12
Preconditioned Conjugate Gradient Method
PCG accuracy
[Hackbusch, Springer, 1994]

## Slide 13: Iterative solver for FE-equation system
with condition number
FE discretization, meshsize:
Example:
[Wolters, Vorlesungsskriptum, Chapter 7.2]
[Wolters, Kuhn, Anwander & Reitzinger, Comp. Vis. Sci.., 2002]
[Lew, Wolters, Dierkes, Roer & MacLeod, Appl.Num.Math., 2009]
Notes: der Tensor muss erklärt werden!!

## Slide 14: Link to this work:
[Wolters, Reitzinger, Basermann, Burkhardt, Hartmann, Kruggel & Anwander, Proceedings of BIOMAG Helsinki, 2000]
Notes: PEBBLES: Parallel and Element Based grey Box Linear Equation Solver

## Slide 15: Iterative solver for FE-equation system
[Wolters, Reitzinger, Basermann, Burkhardt, Hartmann, Kruggel & Anwander, Proceedings of BIOMAG Helsinki, 2000]
Notes: der Tensor muss erklärt werden!!

## Slide 16: Iterative solver for FE-equation system
with condition number
Convergence of the CG solver:
FE discretization, meshsize:
Strategy: Preconditioning!
Example:
[Wolters, Reitzinger, Basermann, Burkhardt, Hartmann, Kruggel & Anwander, Proceedings of BIOMAG Helsinki, 2000]
Notes: c wird asymptotische Konvergenzrate genannt, denn
lim_{i->infty}(c^i\frac{2}{1+c^{2i}})^(1/i)=c
Formel wird mit Hilfe der Chebyshev-Polynome bewiesen und ist nur eine obere Schranke, denn es wird ja \sigma_M=[a,b] gewaehlt, obwohl womoeglich \sigma_M=[a,a´]\cup[b´,b] moeglich waere.

## Slide 17
Jacobi preconditioning
[Wolters, Vorlesungsskriptum, Chapter 7.2]
[Wolters, Kuhn, Anwander & Reitzinger, Comp. Vis. Sci.., 2002]
[Lew, Wolters, Dierkes, Roer & MacLeod, Appl.Num.Math., 2009]

## Slide 18
Incomplete Cholesky preconditioning
[Wolters, Vorlesungsskriptum, Chapter 7.2]
[Wolters, Kuhn, Anwander & Reitzinger, Comp. Vis. Sci.., 2002]
[Lew, Wolters, Dierkes, Roer & MacLeod, Appl.Num.Math., 2009]

## Slide 19
Incomplete Cholesky preconditioning
[Wolters, Vorlesungsskriptum, Chapter 7.2]
[Wolters, Kuhn, Anwander & Reitzinger, Comp. Vis. Sci.., 2002]
[Lew, Wolters, Dierkes, Roer & MacLeod, Appl.Num.Math., 2009]

## Slide 20: MultiGrid (MG) preconditioning
Principle of MG
Smoother for high-frequency error components is effective
[Hackbusch, Springer, 1994]
[Wolters, Vorlesungsskriptum, Chapter 7.2]
[Wolters, Kuhn, Anwander & Reitzinger, Comp. Vis. Sci.., 2002]
[Lew, Wolters, Dierkes, Roer & MacLeod, Appl.Num.Math., 2009]

## Slide 21: MultiGrid (MG) preconditioning
Principle of MG
Smoother for low-frequency error components not effective
[Hackbusch, Springer, 1994]
[Wolters, Vorlesungsskriptum, Chapter 7.2]
[Wolters, Kuhn, Anwander & Reitzinger, Comp. Vis. Sci.., 2002]
[Lew, Wolters, Dierkes, Roer & MacLeod, Appl.Num.Math., 2009]

## Slide 22: MultiGrid (MG) preconditioning
Principle of the MG
Smoother for high-frequency error components
Coarse grid correction for low-frequency error components
[Hackbusch, Springer, 1994]
[Wolters, Vorlesungsskriptum, Chapter 7.2]
[Wolters, Kuhn, Anwander & Reitzinger, Comp. Vis. Sci.., 2002]
[Lew, Wolters, Dierkes, Roer & MacLeod, Appl.Num.Math., 2009]

## Slide 23
MultiGrid (MG) preconditioning
[Hackbusch, Springer, 1994]
[Wolters, Vorlesungsskriptum, Chapter 7.2]
[Wolters, Kuhn, Anwander & Reitzinger, Comp. Vis. Sci.., 2002]
[Lew, Wolters, Dierkes, Roer & MacLeod, Appl.Num.Math., 2009]

## Slide 24: Geometric Multigrid
Geometric MG (GMG)
Problem-specific smoother for high-frequency error components
Coarse grid correction for low-frequency error components
Complexity:
O(N)
Convergence rate:
h-independent
high
Problems in our application
Choice of the smoother is difficult (Inhomogeneities/Anisotropies)
Generation of the coarse grids difficult
Strategy: Algebraic MG (AMG)!
[Hackbusch, Springer, 1994]
[Wolters, Vorlesungsskriptum, Chapter 7.2]
[Wolters, Kuhn, Anwander & Reitzinger, Comp. Vis. Sci.., 2002]
[Lew, Wolters, Dierkes, Roer & MacLeod, Appl.Num.Math., 2009]

## Slide 25: Algebraic Multigrid
Principle of the AMG:
Smoother is given (Gauss-Seidel)
Coarse grids and interpolation matrices are constructed from the entries of K
  Diagonal entries <-> nodes
  Nondiagonal entries <-> edges
Only one high resolution FE mesh!
AMG-interpolation non-optimal:
  Some few error components are not well reduced, i.e., some few eigenvalues of the AMG iteration matrix are close to 1
Problems:
Strategy: AMG-CG!
[Ruge and Stüben, SIAM, 1986; Stüben, GMD, Tech.Report, 1999]
[Wolters, Vorlesungsskriptum, Chapter 7.2]
[Wolters, Kuhn, Anwander & Reitzinger, Comp. Vis. Sci.., 2002]
[Lew, Wolters, Dierkes, Roer & MacLeod, Appl.Num.Math., 2009]

## Slide 26
Preconditioned Conjugate Gradient Method
PCG accuracy
[Hackbusch, Springer, 1994]
[Wolters, Vorlesungsskriptum, Chapter 7.2]
[Wolters, Kuhn, Anwander & Reitzinger, Comp. Vis. Sci.., 2002]
[Lew, Wolters, Dierkes, Roer & MacLeod, Appl.Num.Math., 2009]

## Slide 27: Solver: “Maximal relative error over all eccentricities” versus “solution time”
Nodes: 360,056
Elements: 2,165,281
[Lew, Wolters, Dierkes, Roer & MacLeod, Appl.Num.Math., 2009]
Notes: highlighted

## Slide 28
FE models tuned for subtraction (group 1) and for the direct potential methods (group 2)
[Lew, Wolters, Dierkes, Roer & MacLeod, Appl.Num.Math., 2009]

## Slide 29
Comparison of different preconditioners
[Lew, Wolters, Dierkes, Roer & MacLeod, Appl.Num.Math., 2009]

## Slide 30: Link to this work:
[Wolters, Grasedyck, Anwander & Hackbusch, Biomag, 2004]
Notes: PEBBLES: Parallel and Element Based grey Box Linear Equation Solver

## Slide 31: Efficiency of the fast FE transfer matrix approaches
Head model: Tetrahedral FE, 147,287 nodes, 892,119 elements
[Wolters, Grasedyck, Anwander & Hackbusch, Biomag, 2004]
Notes: der Tensor muss erklärt werden!!

## Slide 32
Head model: Tetrahedral FE, 147,287 nodes, 892,119 elements
Influence space: brain surface mesh, 2mm resolution, 9555 nodes
[Wolters, Grasedyck, Anwander & Hackbusch, Biomag, 2004]
Efficiency of the fast FE transfer matrix approaches
Notes: der Tensor muss erklärt werden!!

## Slide 33
Head model: Tetrahedral FE, 147,287 nodes, 892,119 elements
Influence space: brain surface mesh, 2mm resolution, 9555 nodes
Number of FE forward solutions:
EEG, 71 electrodes: 9555 * 3 = 28665
MEG, 147 channels: 9555 * 2 = 19110 (tangential constraint)
FE approach and dipole model: Venant
[Wolters, Grasedyck, Anwander & Hackbusch, Biomag, 2004]
Efficiency of the fast FE transfer matrix approaches
Notes: der Tensor muss erklärt werden!!

## Slide 34: Parallel AMG-CG on distributed memory computers
``Element-wise’’ partitioning into subdomains
Parallel MultiRHS-AMG-CG: Communication is only necessary for:
Smoother (-Jacobi within interface nodes, Gauss-Seidel between blocks and for inner nodes)
distribution of coarse grid solution
inner products within PCG method
[Wolters, Kuhn, Anwander & Reitzinger, Comp.Vis.Sci, 2002]
Notes: Irregular k way partitioning scheme for irregular graphs

## Slide 35: Results for parallel solver methods
Solver time comparison: Unknowns:147.287
SGI Origin2000, each processor 195MHz, MIPS 10000
Jacobi-CG on 1 proc <-> AMG-CG on 8 procs: Speedup factor of about 80 (10 MG, 8 parallel.)
Anisotropy and inhomogeneity does not change performance results
About a linear speedup for moderate processor number
Stable preconditioning for moderate processor numbers
Distribution of memory
[Wolters, Kuhn, Anwander & Reitzinger, Comp.Vis.Sci, 2002]

## Slide 36
SIM-NEURO work-group at IBB
Thank you for your attention!
Notes: 36
36