## Slide 1: Modern Applied Mathematics in Bioelectromagnetism – Part I
IBB:
Prof. Dr. rer. nat. Carsten Wolters (Coordinator and main responsibility)
Prof. Dr. rer. nat. Joachim Gross (one lecture in SS)
Radiology:
Dr. rer. nat. Jochen Bauer (one lecture in WS and one lecture in SS)
Epilepsy Center Münster-Osnabrück:
PD. Dr. med. Christoph Kellinghaus (one lecture in WS)
Dr. med. Gabriel Möddel (one lecture in SS)
Lecture, Oct.8, 2024
Notes: Tensor weiter erlaeutern
Zeitableitung
Programmlaenge, 1Mill.
WM-Rendering->5000 nodes
1:10 raus und anfangs erwaehnen

## Slide 3: Outline
General planning for this lecture (language? required knowledge? Participants-email-list! target group!)
Literature for this lecture
Introduction to the lecture

## Slide 4: Target group
The course will be offered over two semesters (winter semester 2024/25 and summer semester 2025). The following applications are available: - MSc Mathematics, PO 2020, Specialization "Scientific Computing", Type I - MSc Mathematics, PO 2020, broadening (area of applied mathematics) - BSc Mathematics, PO 2020, broadening (specialization in modeling and analytical methods) - BSC Mathematics, PO 2020, advanced supplement Modeling and Numerical Methods In these cases, the lecture parts of both semesters (4 SWS in total) and the exercise parts of both semesters (2 SWS in total) must be completed, the exercises for both exercise parts must be passed and an oral exam on everything must be taken. The following other possible uses exist: - MSc Mathematics, PO 2020, specialization "Scientific Computing", type II. In this case, the lecture parts of both semesters (4 SWS in total) have to be passed and a reduced course work (from the possibilities of the examination regulations) has to be done, whose form and extent will be announced by Prof. Dr. Carsten Wolters at the beginning of the course. The QISPOS registrations will not take place until the summer semester 2025, when the respective supplementary parts to the lecture and the exercises are also offered.

## Slide 5: Lecture planning for Part I

## Slide 6: Lecture planning for Part I

## Slide 7: Outline
General planning for this lecture (language? required knowledge? Participants-email-list!)
Literature for this lecture
Introduction to the lecture

## Slide 8: Literature for this lecture
Lecture webside: http://www.sci.utah.edu/~wolters/LiteraturZurVorlesung/
Notes: PEBBLES: Parallel and Element Based grey Box Linear Equation Solver

## Slide 9: Link for literature to own work:
Links to all PhD, Master and Bachelor theses and to lecture scriptum
All own publications
Notes: PEBBLES: Parallel and Element Based grey Box Linear Equation Solver

## Slide 10
[Vorwerk, Cho, Rampp, Hamer, Knösche & Wolters, NeuroImage, 2014]
Link for literature to own work:
Notes: 10

## Slide 11: Outline
General planning for this lecture (language? required knowledge? Participants-email-list!)
Literature for this lecture
Introduction to the lecture

## Slide 12
Main steps for brain stimulation: Setup of head model, targeting, optimization of stimulation
Part I will focus on head modeling and EEG/MEG neuroimaging (non-invasive targeting):
  Short history of important bioelectromagnetism- or neuroimaging-methods
  Evoked responses and non-invasive source analysis
Introduction to the lecture: Part I

## Slide 13: Setup of head model
[Vorwerk, Cho, Rampp, Hamer, Knösche & Wolters, NeuroImage, 2014]
Notes: 13

## Slide 14
[Vorwerk, Cho, Rampp, Hamer, Knösche & Wolters, NeuroImage, 2014]
[Wolters, Anwander, Tricoche, Weinstein, Koch & MacLeod, NeuroImage, 2006]
Setup of head model
Notes: 14

## Slide 15
[Wagner, Burger & Wolters, SIAM J. Appl. Math., 2016]
[Schmidt, Wagner, Burger, van Rienen & Wolters, J. Neur. Eng., 2015]
Targeting
[Wagner, Burger & Wolters, SIAM J. Appl. Math., 2016]
[Schmidt, Wagner, Burger, van Rienen & Wolters, J. Neur. Eng., 2015]
[Wagner, PhD thesis in Mathematics, WWU Münster, 2015]
Notes: Segmented MRI (upper row), T1 MRI (middle row) and the source space points (blue points) shown on T1 (lower row) MRI.
Sagittal (left column), coronal (middle column) and axial (right column) slices.
Please note that the slices selected in the lower row are different from the top two rows in order to better visualize the source space points.
The color codes for the 7CA tissues are scalp (green), skull compacta (brown), skull spongiosa (beige), dura mater (dark turquoise), CSF (light turquoise), gray matter (burgundy) and white matter (red).

## Slide 16
[Wagner, Burger & Wolters, SIAM J. Appl. Math., 2016]
[Schmidt, Wagner, Burger, van Rienen & Wolters, J. Neur. Eng., 2015]
Optimization of stimulation
[Wagner, Burger & Wolters, SIAM J. Appl. Math., 2016]
[Schmidt, Wagner, Burger, van Rienen & Wolters, J. Neur. Eng., 2015]
[Wagner, PhD thesis in Mathematics, WWU Münster, 2015]
Notes: Segmented MRI (upper row), T1 MRI (middle row) and the source space points (blue points) shown on T1 (lower row) MRI.
Sagittal (left column), coronal (middle column) and axial (right column) slices.
Please note that the slices selected in the lower row are different from the top two rows in order to better visualize the source space points.
The color codes for the 7CA tissues are scalp (green), skull compacta (brown), skull spongiosa (beige), dura mater (dark turquoise), CSF (light turquoise), gray matter (burgundy) and white matter (red).

## Slide 17
[Wagner, Burger & Wolters, SIAM J. Appl. Math., 2016]
[Schmidt, Wagner, Burger, van Rienen & Wolters, J. Neur. Eng., 2015]
[Wagner, Burger & Wolters, SIAM J. Appl. Math., 2016]
[Schmidt, Wagner, Burger, van Rienen & Wolters, J. Neur. Eng., 2015]
[Wagner, PhD thesis in Mathematics, WWU Münster, 2015]
Optimization of stimulation
Notes: Segmented MRI (upper row), T1 MRI (middle row) and the source space points (blue points) shown on T1 (lower row) MRI.
Sagittal (left column), coronal (middle column) and axial (right column) slices.
Please note that the slices selected in the lower row are different from the top two rows in order to better visualize the source space points.
The color codes for the 7CA tissues are scalp (green), skull compacta (brown), skull spongiosa (beige), dura mater (dark turquoise), CSF (light turquoise), gray matter (burgundy) and white matter (red).

## Slide 18
Main steps for brain stimulation: Setup of head model, targeting, optimization of stimulation
Part I will focus on head modeling and non-invasive targeting:
  Short history of important bioelectromagnetism- or neuroimaging-methods
  Evoked responses and non-invasive source analysis
Introduction to the lecture: Part I

## Slide 19
Institute for Biomagnetism and Biosignalanalysis (IBB)
Bioelectromagnetism-research:
Electroencephalography (EEG)
Magnetoencephalography (MEG)
Magnetic Resonance Imaging (MRI)
Transcranial Electric Stimulation (TES)
Transcranial Magnetic Stimulation (TMS)
Notes: Cohen et al. measured first MEG in 1968: alpha-activity is about 10^7 times weaker than the earth magnetic field

## Slide 20: Measurement and analysis of EEG/MEG and MRI data
304 channel MEG
128 channel EEG
3Tesla Research-MRI

## Slide 21
Hans Berger
1873-1941
Neurologist and psychiatrist
3 times nominated for Nobel-price
1924: First EEG in Jena
Short history of electroencephalography (EEG)

## Slide 22
David Cohen (Physiker)
2010 in Boston/USA
Short history of magnetoencephalography (MEG)
Notes: Cohen et al. measured first MEG in 1968: alpha-activity is about 10^7 times weaker than the earth magnetic field

## Slide 23
David Cohen (Physicist)
1968: Measured the first MEG at MIT in Boston/USA
Short history of magnetoencephalography (MEG)
Notes: From left to right: Edgar Edelsack, David Cohen and James Zimmermann

## Slide 24
David Cohen (Physicist)
1968: Measured the first MEG at MIT in Boston/USA
Short history of magnetoencephalography (MEG)
Notes: From left to right: Edgar Edelsack, David Cohen and James Zimmermann

## Slide 25
Peter Mansfield (Physicist), Paul Lauterbur (Chemist)
1971: developed MRI as imaging modality
Nobel-price of physiology/medicine (2003) for MRI work
Short history of magnetic resonance imaging (MRI)
Notes: Grundlagen des Bildkontrastes:
Unterschiedliche Relaxationszeiten verschiedener Gewebearten
Unterschiedlicher Gehalt an Wasserstoff-Atomen in verschiedenen Geweben (Haut, Schädel)
Zwei grundlegende Ideen:
Einführung von Gradientenfeldern in das konventionelle NMR-Experiment, um NMR-Signale bestimmten räumlichen Bereichen zuzuordnen (Ortskodierung)
Durch gefilterte Rückprojektion ein Abbild des Untersuchungsobjekts errechnen

## Slide 26
Main steps for brain stimulation: Setup of head model, targeting, optimization of stimulation
Part I will focus on head modeling and non-invasive targeting:
  Short history of important bioelectromagnetism- or neuroimaging-methods
  Evoked responses and non-invasive source analysis
Introduction to the lecture: Part I

## Slide 27: The concept of evoked potentials and fields using the example of somatosensory evoked potentials (SEP) and fields (SEF)

## Slide 28
Somatosensory evoked potentials (SEP) and fields (SEF)
[Grottke, Bachelor thesis in Physics, WWU Münster, 2015]

## Slide 29
Somatosensory evoked potentials (SEP) and fields (SEF)
[Grottke, Bachelor thesis in Physics, WWU Münster, 2015]

## Slide 30
S1 and M1 homunculi

## Slide 31
Somatosensory evoked potentials (SEP) and fields (SEF)
[Piastra, PhD thesis, 2019]
Electric stimulation of the medianus nerve
Combined MEG/EEG
Notes: 31

## Slide 32
Somatosensory evoked potentials (SEP) and fields (SEF)
MEG sensor MLP33: Field strength over time
[Piastra, PhD thesis, 2019]
EEG electrode CP3: Potential difference to reference electrode at Cz over time
Notes: 32

## Slide 33
[Piastra, PhD thesis, 2019]
MEG sensor MLP33: Field strength over time
EEG electrode CP3: Potential difference to reference electrode at Cz over time
SEF
SEP
Somatosensory evoked potentials (SEP) and fields (SEF)
Notes: 33

## Slide 34
[Piastra, PhD thesis, 2019]
SEF at sensor MLP33: Field strength over time
SEP electrode CP3: Potential difference to reference electrode at Cz over time
Somatosensory evoked potentials (SEP) and fields (SEF)
SEF and SEP butterfly plots over all sensors
Notes: 34

## Slide 35
[Piastra, PhD thesis, 2019]
Somatosensory evoked potentials (SEP) and fields (SEF)
SEF topography at 20 ms post-stimulus:
N20m component
SEP topography at 20 ms post-stimulus:
P20/N20 component
SEF and SEP butterfly plots over all sensors
Notes: 35

## Slide 36: The concept of evoked potentials and fields using the example of auditory evoked potentials (AEP) and fields (AEF)

## Slide 37
Evoked responses
[Gazzaniga, Ivry & Mangun, Cognitive Neuroscience, 2nd ed., W.W.Norton & Company, 2002]

## Slide 38
Auditory evoked potential (AEP)
[Gazzaniga, Ivry & Mangun, Cognitive Neuroscience, 2nd ed., W.W.Norton & Company, 2002]
Only contralateral path is shown.

## Slide 39
AEP-N1 component
[Okamoto, Stracke, Wolters, Schmael & Pantev, J Neurosci, 2007]
N100 component of AEP/AEF
AEF-N1 component

## Slide 40
Reconstruction of neuronal networks using
EEG and MEG source analysis
Model for the sources
The forward problem
The inverse problem

## Slide 41: Gray and White Matter
Gray matter
(GM)
White matter (WM)
T1 weighted Magnetic Resonance
Image (T1-MRI)
Notes: Cortex:
=====
The neo- or isocortex, i.e., 90% of the cerebral cortex, has a 6 layered structure.
Source model:
=========
1.000.000 activated pyramidal dendrites -> 1.000.000x5x10^{-5} nAm=50nAm
Density of pyramidal cells in the cortex=1.000.000/30mm^2=33.333 pyramidal cells/mm^2

## Slide 42: The source model
+
-
-
cell body
sink
source
~30 mm2 = 5.5×5.5 mm2
Size of Macroscopic Neural Activity
Equivalent Current Dipole (Primary current) (~50 nAm)
parameters:
position : x0
moment : M
cortex
synapse
-
+
Microscopic current flow (~5×10-5 nAm)
Notes: 1.000.000 activated pyramidal dendrites -> 1.000.000x5x10^{-5} nAm=50nAm
Density of pyramidal cells in the cortex=1.000.000/30mm^2=33.333 pyramidal cells/mm^2
1mm^2 activated tissue produces magnetic field of 0.1pT=0.1*10^{-12}T (Okada in turtle brain)

## Slide 43
Reconstruction of neuronal networks using
EEG and MEG source analysis
Model for the sources
The forward problem
The inverse problem

## Slide 44
Maxwell equations
Notes: D: elektrische Flussdichte
E: elektrische Feldstärke
H: magnetische Feldstärke
B: magnetische Flussdichte
Verlauf der elektrischen Feldstärke zeigt die Richtung der vom Feld ausgeübten Kraft an und Feldliniendichte stellt die Feldstärke dar.
Beim magnetischen Feld wirkt die Kraft senkrecht zur Richtung der magnetischen Flussdichte.
In Quellenfeldern zeichnen sich die Feldlinien durch einen Anfang und ein Ende aus (oder verschwinden im Unendlichen).
In Wirbelfeldern sind die Feldlinien geschlossene Kurven.
Induktionsgesetz von Faraday

## Slide 45: EEG forward problem
Compute the EEG
Place a dipole
Simulate
quasistatic
Maxwell equations
[Wolters & de Munck, Scholarpedia, 2007]
[de Munck, Wolters & Clerc, In: Handbook of neural activity measurement, 2012]
Notes: 42 year old female suffering from medically intractable complex partial seizures of mesial-temporal origin
Seizures had duration of up to 10 minutes and a frequency of twice to 5 times a month
Measurements:
=========
A short-term barbiturate (Schlafmittel), known to provoke epileptiform activity
-> 60-channel EEG montage with reference at the ear contralateral to the epileptic focus
Source reconstruction:
==============
Single dipole fit at signal peak
->Localization of the secondary activations, propagating along the temporal cortical surface
->Primary activity in the hippocampus and the amygdala (cannot be measured outside)
Therapy:
======
Selective amygdalohippocampectomy
-> Patient free of seizures

## Slide 46: MEG forward problem
Compute the MEG
Place a dipole
Simulate
quasistatic
Maxwell equations
[Wolters & de Munck, Scholarpedia, 2007]
[de Munck, Wolters & Clerc, In: Handbook of neural activity measurement, 2012]

## Slide 47: Multi-compartment volume conductor model
Skin | 0.33 S/m
Skull | anisotropic/ 3-layer
CSF | 1.79 S/m
Gray matter | 0.33 S/m
White matter | anisotropic
[Wolters & de Munck, Scholarpedia, 2007]
[de Munck, Wolters & Clerc, In: Handbook of neural activity measurement, 2012]

## Slide 48: Three-layered human skull

## Slide 49: Anisotropy of white matter (WM)
Longitudinally: 9
Transversally: 1

## Slide 50: Volume conductor modeling
Spherical shells
 | Geometry | Conductivity
Skin | unreal. | unreal.
Skull | unreal. | unreal.
CSF | unreal. | unreal.
GM | unreal. | unreal.
WM | unreal. | unreal.
 | Geometry | Conductivity
Skin | realistic | realistic
Skull | realistic | unreal.
CSF | unrealistic (1 isotropic value) | 
GM |  | 
WM |  | 
Boundary element
Finite Element (FE)
 | Geometry | Conductivity
Skin | realistic | realistic
Skull | realistic | realistic
CSF | realistic | realistic
GM | realistic | realistic
WM | realistic | realistic

## Slide 51: Realistically shaped multi-compartment anisotropic head volume conductor modeling for accurate simulation in EEG/MEG and tCS/TMS
[Wolters, Anwander, Tricoche, Weinstein, Koch & MacLeod, NeuroImage, 2006]
[Vorwerk, Cho, Rampp, Hamer, Knösche & Wolters, NeuroImage, 2014]
[Wagner, Rampersad, Aydin, Vorwerk, Oostendorp, Neuling, Herrmann, Stegeman & Wolters, J. Neur. Eng., 2014]
Notes: 51

## Slide 52: The forward problem in EEG/MEG
[Wolters & de Munck, Scholarpedia, 2007]
[de Munck, Wolters & Clerc, In: Handbook of neural activity measurement, 2012]
potential distribution
or current
Simulate
Notes: 52

## Slide 53
Reconstruction of neuronal networks using
EEG and MEG source analysis
Model for the sources
The forward problem
The inverse problem

## Slide 54
SEP-P20
SEF-P20
Source analysis: The inverse Problem
Reconstruct
source
[Antonakakis, Schrader, Wollbrink, Oostenveld, Rampp, Haueisen & Wolters, HBM, 2019]

## Slide 55
SEP-P20
SEF-P20
Reconstruct
source
Source analysis: The inverse Problem
[Antonakakis, Schrader, Wollbrink, Oostenveld, Rampp, Haueisen & Wolters, HBM, 2019]

## Slide 56: Thank you for your attention!
Notes: 56